# Text boxes

Materials

Support Base:  17" circular base, injected molded polypropylene, with 227 sq. in. of surface on bottom, designed for weight displacement.

Base Dimensions: 3"H X 17" in diameter, designed for weight displacement, with molded insert for square tubing and two threaded rod couplings molded in.

LEED: Minimum 40 % post industrial recycled polypropylene with UV inhibitors.

Platform: 4” X 4” Angle Iron frame, coped and welded; 1” X 3/16” bar grating, 19-W-4 carbon steel, ends capped with 1” X 1/ 4” steel flat bar; Legs are made of 3” X 3” tubular steel. Hot-Dip Galvanized after fabrication.

Handrails:  1-1/2” schedule 40 pipe, welded; fastened to platform by flat plat connection.

Hardware:  3/4” X 2-1/2” Bolts with 3/4” Nuts and Washers; Grating Clips with 1-1/2 “ Self Tapping Screws; available in Pre-Galvanized Zinc coated or Hot-Dip Galvanized.

Accessories:  Protection Pads, ladder/stairs, telco rack, cable hangers

ASP1410ELH – Elevated Equipment Platform – Is designed to support telecommunications equipment or HVAC equipment in flood plain areas or where heights of 3 feet or above are required.  Cross bracing is added on heights of 6 feet or higher.  Custom sizes and heights are available.

This print/image and design and detail shown hereon is the property of Advanced Support Products, Inc. This print is furnished with the understanding that it is not to be reproduced without permission, and must be returned upon demand.  All rights of design and invention are reserved by Advanced Support Products.      Patents #5816554 ;  #6229497;  #6427965;  #6448497;  #6578827  © 2010

Installation:

- Verify that surface is smooth and clean to extent needed to receive materials.

- Review approved final drawings to determine the locations of Platform.

- Clean surfaces to receive 17” support bases removing any foreign matter before setting 17” circular support bases.

- Accurately locate Base Platform in location specified as per approved shop drawings or as required herein and by site conditions. No Isolation pads are required under the 17" circular bases.

- Assemble platform according to approved drawings and instructions supplied by manufacturer.

- Insert steel frame structures into 17" circular bases as indicated in above drawing.

- Attach handrails, stairs, ladders or other accessories according to instructions supplied by manufacturer.

- Adjust height of each support base for equal weight disbursement. Correct if necessary.

- Repeat until all support bases supplied are installed in accordance with approved shop drawings.

- Remove any unused materials and packaging from job site.

Specification Sheet

ASP1410ELH

Elevated Equipment Platform